## Slide 1: RGB COLOR SENSOR PROJECT Team Sagittarius
Final Evaluation - 10th August

## Slide 2: Project targets
Identifying the color of an object
    Display the RGB values
    Output the corresponding color in RGB LED
    ( Sending to remote device - via Bluetooth )
Lighting the RGB LED for a user input color
    Input from keypad
    (Remote user input - via Bluetooth)
Using only 1-PWM pin for RGB LED

## Slide 3: Division of Main Tasks
Task | Index | Name
Sensor and Calibration | 190301H | Karunanayaka Y.S.
User Interface and Display | 190286M | Kajhanan. K.
User Inputs / Keypad | 190280N | Jegakumaran P.
Output RGB LED | 190285J | Kahawalage A.P.P.

## Slide 4: Basic idea of sensor
Using : One white LED + 3 LDRs with RBG filters papers
White LED
LDR with
Green filter
LDR with
Blue filter
LDR with
Red filter
Each color filter lets pass only one main color (R,G or B).
Therefore, using each LDRs resistance values at a given time we can measure the amount of each color reflected from the object.
After experimenting with several calibration procedures, we could detect both primary colors and secondary colors accurately.

## Slide 5: Calibration
CALIBRATION 01 - System calibration (done only once)
  To overcome the differences in each sensor for RED, GREEN, BLUE and keep them in a common ground.
  Done using 9 shades of WHITE , (GREY) to BLACK
CALIBRATION 02 - Calibration considering user expectations
  To map the RGB values user expect and what sensor really recognized
  Done using any color given by user and its expected color composition

## Slide 6: Calibration process explained
Points  Real color intensity
Line  Measured color intensity
Line  Real color intensity
Points  Measured color intensity
Mirror
Samples of nine shades of grey
Calculated
curves

## Slide 7
Grey scale calibration
Calibration done using 9 shades of grey.
A more reliable calibration method because,
  It covers entire 0 – 255 range all 3 fundamental colors
  Calibration material can be accurately printed using any printer
This is the recommended method for the device
Color code calibration
Calibration done by 1-9 codes of colors
The exact color of the material should be known
The calibration calculates the approximation for the most fitting curve.
Not reliable. Because,
  The color code always has an error.
  Same color may change the reflection due to the material.
  Printers cannot accurately print these colors.
Methods of calibration

## Slide 8: User inputs - Keypad
Since still we can not use 7 dedicated pins for the keyboard, we selected 4 pins which are already used for display to send signals. And another 3 pins for the keypad only.
Used to connect columns of keypad
Used to connect BOTH display and keypad rows
We switched 5V to 4 rows then detect the signal from columns. So, we could identify the pressed key specifically.
Because display does not response until Enable Signal is given, there will be no confusion between keypad and display.
--Explaining code--

## Slide 9: Display, Menu and user interface
--Explaining code--
Used to connect display
Managing the limited pins (have to share with keypad)
Reacting to user inputs and updating the display in real time

## Slide 10
1: Sensor
1: Color Input
1: Yes
2: No
2: RGB LED
2: Real Time
(Show sensed color)
* = OK

## Slide 11
Using 1 PWM and 2 digital output pins.
Pin | Task
1 PWM | Setting the corresponding intensity of each color
2 Digital Output Pins | Switching to the right color at the right moment
ATMega 328p
Demux
RGB
LED
PWM
Digital outputs
00  Red
01  Green
10  Blue
G
B
R
GND
Output RGB LED

## Slide 12
ATMega 328p
Demux
RGB
LED
PWM
Digital outputs
00  Red
01  Green
10  Blue
G
B
R
255,255,255
255, 0, 0
128, 50, 200
One Time Frame
For red
For green
For blue
RGB value
PWM time period (50% duty cycle)
At least 10- time frames per second
is required to avoid blinking
Switching freq. 10Hz
T = 0.1s
30Hz
Switching freq. 30Hz
T =33.33ms
Default Max PWM freq. = 980Hz
Totally enough but we obtained the highest frequency as follows

## Slide 13: Getting the maximum switching speed
With the 16MHz oscillator maximum counter with 256 states have the frequency 31.125kHz
8-bit
=
= 31.25kHz

## Slide 14
~32us
And it is working correctly in Proteus
For 128 (50% duty cycle)
5us

## Slide 15: Bluetooth and User Interface for PC
We created a user interface for windows using C#.
Connecting to sensor via Bluetooth.
(Can be disconnected from both pc and sensor itself.)
Calibration
Reading real time color and recording in a log file
Sending a specified color and lighting the LED
Sending any message to display

## Slide 16: PCB Design
Motherboard
Sensor
Sensor - connection
Display - connection
Power
Bluetooth
Keypad - connection

## Slide 17
Enclosure